Article IV.			Post-Construction Storm Water Management Ordinance

Sec. 18-4-1		Purpose

Sec. 18-4-2		Objectives

Sec. 18-4-3		Applicability

Sec. 18-4-4		Definitions

Sec. 18-4-5		Post-Construction Storm Water Management Plan

Sec. 18-4-6		Post-Construction Storm Water Management Plan Compliance

Sec. 18-4-7		Enforcement

Sec. 18-4-8		Notice of Violation

Sec. 18-4-9		Penalties/Fines/Injunctive Relief

Sec. 18-4-10	Consent Agreement

Sec. 18-4-11	Appeal of Notice of Violation

Sec. 18-4-12	Enforcement Measures

Sec. 18-4-13	Severability

Sec. 18-4-1.		Purpose. The purpose of this "Post-Construction Storm Water Management Ordinance" (the "Ordinance") is to provide for health, safety, and general welfare of the citizens of the Town of Cape Elizabeth through review and approval of post-construction storm water management plans and monitoring and enforcement of compliance with such plans as required by Federal and State law.

This Ordinance establishes methods for post-construction storm water management in order to comply with minimum control measure requirements of the Federal Clean Water Act, of federal regulations, of Maine's Small Municipal Separate Storm Sewer Systems General Permit, and the Town’s Storm Water Program Management Plan.

The Town of Cape Elizabeth enacts this Post-Construction Storm Water Management Control Ordinance (the "Ordinance") pursuant to 30-A M.R.S.A. § 3001 (municipal home rule ordinance authority), 38 M.R.S.A. § 413 (the "Wastewater Discharge Law"), 33 U.S.C. § 1251 et seq. (the "Clean Water Act"), and 40 CFR Part 122 (U.S. Environmental Protection Agency's regulations governing the National Pollutant Discharge Elimination System ("NPDES")). The Maine Department of Environmental Protection, through its promulgation of the "General Permit for the Discharge of Storm Water from Small Municipal Separate Storm Sewer Systems," has listed the Town of Cape Elizabeth as having a Regulated Small Municipal Separate Storm Sewer System ("Small MS4"); under this General Permit, listing as a Regulated Small MS4 necessitates enactment of this Ordinance as part of the Town's Storm Water Management Program in order to satisfy the minimum control measures required by Part IV D 5 ("Post-construction storm water management in new development and redevelopment").

Sec. 18-4-2.		Objectives. The objectives of this Ordinance are:

- To reduce the impact of post-construction discharge of storm water on receiving waters; and

- To reduce storm water runoff rates and volumes, soil erosion and nonpoint source pollution, wherever possible, through use of Best Management Practices as promulgated by the Maine Department of Environmental Protection pursuant to its most current rules as may be updated or amended including its Chapters 500 and 502 Rules, and ensure that these management controls are properly maintained and pose no threat to public safety.

Sec. 18-4-3.		Applicability.

This Ordinance applies to all New Development and Redevelopment within the Town that discharges storm water to the Town's Municipal Separate Storm Sewer System (MS4) and to associated storm water management facilities, which are considered to be an element or array of elements that convey water from or across land, including, but not limited to, natural elements, roads, parking areas, catch basins, drainage swales, detention basins and ponds, pipes, conduits, and related structures that are part of the Post-Construction Storm Water Management Plan for a New Development or Redevelopment.

This ordinance does not apply to any development which has obtained subdivision approval and begun construction prior to the date this ordinance becomes effective. Construction shall mean (1) posting of a performance guarantee, (2) disturbance of soil, and (3) inspection by a town official.

Sec. 18-4-4.		Definitions. For the purposes of this Ordinance, the following terms shall have the meanings given herein. All words not defined herein shall carry their customary and usual meanings.

Applicant: Any Person with requisite right, title, or interest or an agent for such Person who has filed an application for New Development or Redevelopment that requires a Post-Construction Storm Water Management Plan under this Ordinance.

Best Management Practices ("BMP"): Any schedule of activities, prohibitions of practices, maintenance procedures, and other management practices to prevent or reduce the pollution of waters of the State of Maine. BMPs also include treatment requirements, operating procedures, and practices to control plant site runoff, spillage or leaks, sludge or waste disposal, or drainage from raw material storage.

Clean Water Act: The federal Water Pollution Control Act (33 U.S.C. § 1251 et seq., also known as the "Clean Water Act"), and any subsequent amendments thereto.

Construction Activity: Any Construction Activity including one acre or more of Disturbed Area. Construction Activity also includes activity with less than one acre of total land Disturbed Area if that area is part of a subdivision that will ultimately disturb an area equal to or greater than one acre.

Discharge: Any spilling, leaking, pumping, pouring, emptying, dumping, disposing, or other addition of Pollutants to Waters of the State.

Direct Discharge: Any discernible, confined and discrete conveyance, including, but not limited to, any pipe, ditch, channel, tunnel, conduit, well, discrete fissure, container, rolling stock, concentrated animal feeding operation or vessel or other floating craft, from which Pollutants are or may be discharged (Also known as Point Source).

Disturbed Area: Any clearing, grading, and excavation. Mere cutting of trees, without grubbing, stump removal, disturbance or exposure of soil is not considered "Disturbed Area." "Disturbed Area" does not include routine maintenance but does include Redevelopment. "Routine Maintenance" is maintenance performed to maintain the original line and grade, hydraulic capacity, and original purpose of land or improvements thereon.

Enforcement Authority: The Town Manager or his/her designee who is the person(s) or department authorized by the Town to administer and enforce this Ordinance.

Town: The Town of Cape Elizabeth.

Town Permitting Authority: The Town official or body that has jurisdiction over the land use approval or permit required for a New Development or Redevelopment.

Municipal Separate Storm Sewer System, or MS4: Conveyances for storm water, including, but not limited to, roads with drainage systems, municipal streets, catch basins, curbs, gutters, ditches, human-made channels or storm drains (other than publicly owned treatment works and combined sewers) owned or operated by any municipality, sewer or sewage district, fire district, State agency or federal agency or other public entity that discharges directly to Waters of the State.

National Pollutant Discharge Elimination Systems (NPDES) Storm Water Discharge Permit: A permit issued by the United States Environmental Protection Agency ("EPA") or by the Maine Department of Environmental Protection ("DEP") that authorizes the Discharge of pollutants to waters of the United States, whether the permit is applicable on an individual, group, or general area-wide basis.

New Development: Any Construction Activity on unimproved Premises and for purposes of this ordinance includes "Redevelopment" defined below.

Person: Any individual, firm, corporation, municipality, town, quasi-municipal Corporation, State or Federal agency, or other legal entity.

Pollutant: Any dredged spoil, solid waste, junk, incinerator residue, sewage, refuse, effluent, solid waste , sewage sludge, munitions, chemicals, biological or radiological materials, oil, petroleum products or by-products, heat, wrecked or discarded equipment, aggregate materials, and industrial, municipal, domestic, commercial or agricultural wastes of any kind.

Post-Construction Storm Water Management Plan: BMPs and associated inspection and maintenance procedures for the Storm Water Runoff System employed by a New Development or Redevelopment to meet the standards of this Ordinance and approved by the Town’s Permitting Authority.

Premises: Any building, lot, parcel of land, or portion of land, whether improved or unimproved, including adjacent sidewalks and parking strips, located within the Town from which Discharges into the Town Storm Water Runoff System are or may be created, initiated, originated, or maintained.

Qualified Post-Construction Storm Water Inspector: A person who conducts post-construction inspections of Storm Water Runoff Systems and meets the following qualification:

- The Inspector shall not have any ownership or financial interest in the property being inspected nor be an employee or partner of any entity having an ownership or financial interest in the property, and

- The Inspector shall also meet the following criteria as approved by the Town’s Enforcement Authority:

  - Someone who has received the appropriate training for such inspection from DEP and holds a valid certificate from DEP for such inspection or;

  - Have a working knowledge of the most current Maine DEP Storm Water Management Laws including but not limited to Chapter 500 and Chapter 502 Rules, Storm Water Management Rules and Maine's Storm Water BMP Manual, have a college degree in environmental science, civil engineering, or comparable expertise, or any combination of experience and training; have a demonstrated practical working knowledge of Storm Water hydrology and Storm Water management techniques, including the maintenance requirements for Storm Water Runoff Systems; and have the ability to determine if Storm Water Runoff Systems are performing as intended;

Redevelopment: Any Construction Activity on Premises already improved with buildings, structures, or activities or uses, but does not include such activities as exterior remodeling of structures.

Regulated Small MS4: Any Small MS4 regulated by the State of Maine "General Permit for the Discharge of Storm Water from Small Municipal Separate Storm Sewer Systems" ("General Permit"), including all those located partially or entirely within an Urbanized Area (UA) and those additional Small MS4s located outside a UA that as of the issuance of the General Permit have been designated by the DEP as Regulated Small MS4s.

Small Municipal Separate Storm Sewer System, or Small MS4: Any MS4 that is not already covered by the Phase I MS4 Storm Water program including municipally owned or operated storm sewer systems, State or federally-owned systems, such as colleges, universities, prisons, Maine Department of Transportation and Maine Turnpike Authority road systems and facilities, and military bases and facilities.

Storm Water: Runoff resulting from snowmelt, rain, precipitation, groundwater on the ground and drainage.

Storm Water Runoff System:  An element or array of elements that convey water from or across land, including, but not limited to, natural elements.

Urbanized Area ("UA") means the areas of the State of Maine as defined by the latest decennial census by the U.S. Bureau of the Census.

Sec. 18-4-5.		Post-Construction Storm Water Management Plan.

- General Requirement

  - Except as provided in Sec. 18-4-3 b. above, no Applicant for a building permit, subdivision approval, site plan approval or other zoning, planning or other land use approval for New Development or Redevelopment to which this Ordinance is applicable shall receive such permit or approval for that New Development or Redevelopment unless the Town Permitting Authority for that New Development also determines that the Applicant's Post-Construction Storm Water Management Plan for the New Development meets the requirements of this Ordinance.

  - At the time of application, the Applicant shall notify the Town Permitting Authority if its Post-Construction Storm Water Management Plan includes any BMP(s) that will discharge to the Town's MS4 and shall include in this notification a listing of which BMP(s) will so discharge.

- Performance Standards

  - The Applicant shall make adequate provisions for the management of the quantity and quality of all storm water generated by a New Development or Redevelopment through a Post-Construction Storm Water Management Plan. This Post-Construction Storm Water Management Plan shall be designed to meet the standards contained in the Maine Department of Environmental Protection's most current rules as may be updated or amended including its Chapters 500 and 502 Rules and shall comply with the practices described in the manual Storm Water Management for Maine, published by Maine Department of Environmental Protection, latest edition, which hereby are incorporated by reference pursuant to 30-A M.R.S.A. § 3003.

  - The Applicant shall meet the quantity and quality standards above either on-site or off-site. Where off-site facilities are used, the Applicant must submit to the Town documentation, approved as to legal sufficiency by the Town's attorney, that the Applicant has a sufficient property interest in the property where the off-site facilities are located – by easement, covenant or other appropriate legal instrument – to ensure that the facilities will be able to provide post-construction storm water management for the New Development or Redevelopment and that the property will not be altered in a way that interferes with the off-site facilities.

  - Where the Applicant proposes to retain ownership of the Storm Water Management Facilities shown in its Post-Construction Storm Water Management Plan, the Applicant shall submit to the Town documentation, approved as to the legal sufficiency the Town's attorney that the Applicant, it successor, heirs and assigns shall have the legal obligation and the resources available to operate, repair, maintain and replace the Storm Water Management Facilities. Applications for New Development or Redevelopment requiring Storm Water Management Facilities that will not be dedicated to the Town shall enter into a Maintenance Agreement with the Town. A sample of this Maintenance Agreement is available from the Town.

  - Whenever elements of the Storm Water Runoff System are not within the right-of-way of a public street and the facilities will not be offered to the Town for acceptance as public facilities, the Town Permitting Authority may require that perpetual easements conforming substantially with the lines of existing natural drainage, and providing adequate access for maintenance in a form acceptable to the Town's attorney, shall be provided to the Town allowing access for maintenance, repair, replacement and improvement of the Storm Water Runoff System. When an offer of dedication is required by the Town Permitting Authority, the Applicant shall be responsible for the maintenance of these Storm Water Runoff Systems under this Ordinance until such time (if ever) as they are accepted by the Town.

  - In addition to any other applicable requirements of this Ordinance and the Town's Municipal Code, any New Development or Redevelopment which also requires a storm water management permit from the Maine Department of Environmental Protection (DEP) under 38 M.R.S.A. 420-D shall comply with the rules adopted by DEP under 38 M.R.S.A. 420-D(1), as the same may be amended from time to time, and the Applicant shall document such compliance to the Town Permitting Authority. Where the standards or other provisions of such storm water rules conflict with Town ordinances, the stricter (more protective) standard shall apply.

Sec. 18-4-6	.	Post-Construction Storm Water Management Plan Compliance.

- General Requirements. Any Person owning, operating, leasing or having control over Storm Water Runoff Systems required by a Post-Construction Storm Water Management Plan approved under this Ordinance shall demonstrate compliance with that Plan as follows:

  - A Qualified Post-Construction Storm Water Inspector , shall, at least annually, inspect the Storm Water Runoff Systems, including but not limited to any roads, parking areas, catch basins, drainage swales, detention basins and ponds, pipes, conduits, and related structures, in accordance with all Town and State inspection, cleaning and maintenance requirements of the approved Post-Construction Storm Water Management Plan.

  - If the Storm Water Runoff Systems require maintenance to function as intended by the approved Post-Construction Storm Water Management Plan, that Person shall take corrective action(s) to address the deficiency or deficiencies.

  - A Qualified Post-Construction Storm Water Inspector shall provide, on or by May  1 of each year, a completed and signed certification to the Town Enforcement Authority in a form prescribed by the Town or in a similar form approved by the Town Enforcement Authority, certifying that the Storm Water Runoff Systems have been inspected, and that they are adequately maintained and functioning as intended by the approved Post-Construction Storm Water Management Plan, or that they require maintenance or repair, describing any required maintenance and any deficiencies found during inspection of the Storm Water Runoff Systems. If the Storm Water Runoff Systems require maintenance or repair of deficiencies in order to function as intended by the approved Post-Construction Storm Water Management Plan, the Person shall provide a record of the required maintenance or deficiency and corrective action(s) taken.

  - In addition, any persons required to file an annual certification under this Sec. 18-4-6 of this Ordinance shall include with the annual certification a fee established by the Town Council in accordance with the Town Fee Schedule. The purpose of this fee is to pay the administrative and technical costs of review of the annual certification.

- Right of Entry. In order to determine compliance with this Ordinance and with the Post-Construction Storm Water Management Plan, the Town Enforcement Authority may enter upon property at reasonable hours with the consent of the owner, occupant or agent to inspect the Storm Water Runoff Systems.

- Annual Report. Beginning July 1, 2010 and each year thereafter, the Town shall include the following in its Annual Report to the Maine Department of Environmental Protection:

  - The cumulative number of sites that have Storm Water Runoff Systems discharging into their MS4;

  - A summary of the number of sites that have Storm Water Runoff Systems discharging into their MS4 that were reported to the Town;

  - The number of sites with documented functioning Storm Water Runoff Systems; and

  - The number of sites that required routine maintenance or remedial action to ensure that Storm Water Runoff Systems are functioning as intended.

Sec. 18-4-7.		Enforcement. It shall be unlawful for any Person to violate any provision of or to fail to comply with any of the requirements of this Ordinance or of the Post-Construction Storm Water Management Plan. Whenever the Enforcement Authority believes that a Person has violated this Ordinance or the Post-Construction Storm Water Management Plan, the Enforcement Authority may enforce this Ordinance in accordance with 30-A M.R.S.A. § 4452.

Sec. 18-4-8.		Notice of Violation. Whenever the Enforcement Authority believes that a Person has violated this Ordinance of the Post-Construction Storm Water Management Plan, the Enforcement Authority may order compliance with this Ordinance or with the Post-Construction Storm Water Management Plan by written notice of violation to that Person indicating the nature of the violation and ordering the action necessary to correct it, including, without limitation:

- The abatement of violations, and the cessation of practices, or operations in violation of this Ordinance or of the Post-Construction Storm Water Management Plan;

- At the Person's expense, compliance with BMPs required as a condition of approval of the New Development or Redevelopment, the repair of Storm Water Runoff Systems and/or the restoration of any affected property; and/or

- The payment of fines, of the Town's remediation costs and of the Town's reasonable administrative costs and attorneys' fees and costs.

If abatement of a violation, compliance with BMPs, repair of Storm Water Management Facilities and/or restoration of affected property is required, the notice shall set forth a deadline within which such abatement, compliance, repair and/or restoration must be completed.

Sec. 18-4-9.		Penalties/Fines/Injunctive Relief.  Any Person who violates this Ordinance of the Post-Construction Storm Water Management Plan shall be subject to fines, penalties and orders for injunctive relief and shall be responsible for the Town's attorney's fees and costs, all in accordance with 30-A M.R.S.A. § 4452. Each day that such violation continues shall constitute a separate violation. Moreover, any Person who violates this Ordinance or the Post-Construction Storm Water Management Plan also shall be responsible for any and all fines, penalties, damages and costs, including, but not limited to attorneys' fees and costs, incurred by the Town for violation of federal and State environmental laws and regulations caused by or related to that Person's violation of this Ordinance or of the Post-Construction Storm Water Management Plan; this responsibility shall be in addition to any penalties, fines or injunctive relief imposed under this Section.

Sec. 18-4-10.	Consent Agreement. The Enforcement Authority may, with the approval of the municipal officers, enter into a written consent agreement with the violator to address timely abatement of the violation(s) of this Ordinance or of the Post-Construction Storm Water Management Plan for the purposes of eliminating violations of this Ordinance or of the Post-Construction Storm Water Management Plan and of recovering fines, costs and fees without court action.

Sec. 18-4-11.	Appeal of Notice of Violation. Any Person receiving a Notice of Violation or suspension notice may appeal the determination of the Enforcement Authority to the Zoning Board of Appeals. The notice of appeal must be received within 30 days from the date of receipt of the Notice of Violation.

The Board of Appeals shall hold a de novo hearing on the appeal within 30 days from the date of receipt of the notice of appeal. The Board of Appeals may affirm, reverse or modify the decision of the Enforcement Authority. A party aggrieved by the decision of the Board of Appeals may appeal that decision to the Maine Superior Court within 45 days of that date of the Board of Appeals decision pursuant to Rule 80B of the Maine Rules of Civil Procedure.

Sec. 18-4-12.	Enforcement Measures. If the violation has not been corrected pursuant to the requirements set forth in the Notice of Violation, or, in the event of an appeal to the Board of Appeals, within 45 days of a decision of the Board of Appeals affirming or modifying the Enforcement Authority's decision, then the Enforcement Authority may recommend to the municipal officers that the Town's attorney file an enforcement action in a Maine court of competent jurisdiction under Rule 80K of the Maine Rules of Civil Procedure.

Sec. 18-4-13.	Severability. The provisions of this Ordinance are hereby declared to be severable. If any provision, clause, sentence, or paragraph of this Ordinance or the application thereof to any person, establishment, or circumstances shall be held invalid, such invalidity shall not affect the other provisions, clauses, sentences, or paragraphs or application of this Ordinance.

Maintenance Agreement for

Storm Water Runoff Systems

This Maintenance Agreement is made this 		 day of 				 20     by and between 						__________, ______________________________________(address), _______________(phone), __________________________(e-mail), its successor, heirs and assigns and the Town of Cape Elizabeth, Maine.

The project name is 											.

The location is: 									, Cape Elizabeth, Maine.

The project's Tax Map _________and Lot Numbers are Tax Map Lot 		.

The project is shown on a plan entitled "						" dated 			 and most recently revised on 			, approved by the 					 [Municipal Permitting Board] on 			 and recorded in the 				 County Registry of Deeds in Plan Book 			 Page 		 (the "Project").

WHEREAS, the approval of the Project includes Storm Water Runoff Systems which requires periodic maintenance; and

WHEREAS, in consideration of the approval of the Project the Town of Cape Elizabeth requires that periodic maintenance be performed on the Storm Water Runoff Systems;

NOW, THEREFORE, in consideration of the mutual benefits accruing from the approval of the Project by the Town and the agreement of 					 to maintain the Storm Water Runoff Systems, the parties hereby agree as follows:

- , for itself, and its successors and assigns, agrees to the following:

(a)	Annually inspect, clean, maintain, and repair the Storm Water Runoff Systems, which includes, to the extent they exist, roads, parking areas, catch basins, detention basins or ponds, drainage swales, pipes and related structures, at least annually, to prevent the build-up and storage of sediment and debris in the system.

(b) To repair any deficiencies in the Storm Water Runoff Systems noted during the annual inspection;

(c) To provide a summary report on the inspection, maintenance and repair activities performed annually on the Storm Water Runoff Systems to the Town Enforcement Authority;

(d) To allow access by Town personnel or the Town's designee for inspecting the Storm Water Runoff Systems for conformance with these requirements.

(e) To create a homeowners' association for the purposes of maintaining the Storm Water Runoff Systems.

- Upon creation of the homeowners' association, the homeowners' association shall become responsible for compliance with the terms of this Agreement.

- This Agreement shall constitute a covenant running with the land, and 				 shall reference this Agreement in all deeds to lots and/or units within this Project.

By:

Witness										Its:

TOWN OF CAPE ELIZABETH

By:

Witness										Its:

STATE OF MAINE

, ss.									, 20

Personally appeared the above-named 							, the

of 							, and acknowledged the foregoing Agreement to be said person's free act and deed in said capacity.

Before me,

Notary Public / Attorney at Law

Print Name:

STATE OF MAINE

, ss.									, 20

Personally appeared the above-named 							, the

of the Town of Cape Elizabeth, and acknowledged the foregoing Agreement to be said person's free act and deed in said capacity.

Before me,

Notary Public / Attorney at Law

Print Name:

STATE OF MAINE

, ss.									, 20

Annual Storm Water Runoff Systems Certification

(to be sent to Town's Enforcement Authority)

I, 										 (print or type name)    ________________________________________(address), _________________(phone), _____________________________(e-mail), certify the following:

- I am making this Annual Storm Water Runoff Systems Certification for the following property: 													 (print or type name of subdivision, condominium or other development) located at 														 (print or type address), (the "Property");

- The owner, operator, tenant, lessee or homeowners' association of the Property is 															 (name(s) of owner, operator, tenant, lessee, homeowners' association or other party having control over the Property);

- I am the owner, operator, tenant, lessee, or president of the homeowners' association, or am a Qualified Post-Construction Storm Water Inspector hired by the same (circle one);

- I have knowledge of erosion and storm water control and have reviewed the approved Post-Construction Storm Water Management Plan for the Property;

- On 							, 20	, I inspected or had inspected by 		            , (name)________________________________________(address), _________________(phone), _____________________________(e-mail), a Qualified Post-Construction Storm Water Inspector, the Storm Water Runoff Systems, including but not limited to roads, parking areas, catch basins, drainage swales, detention basins and ponds, pipes and related structures required by the approved Post-Construction Storm Water Management Plan for the Property;

- At the time of my inspection of the Storm Water Runoff System on the Property, I or the Qualified Post-Construction Storm Water Inspector identified the following need(s) for routine maintenance or deficiencies in the Storm Water Runoff Systems:

- On 							, 20	, I took or had taken the following routine maintenance or the following corrective action(s) to address the deficiencies in the Storm Water Runoff Systems stated in 6. Above:

- As of the date of this certification, the Storm Water Runoff Systems are functioning as intended by the approved Post-Construction Storm Water Management Plan for the Property.

Date:								, 20		By:

Signature

Print Name

STATE OF MAINE

, ss.									, 20

Personally appeared the above-named 							, the

of 							, and acknowledged the foregoing Agreement to be said person's free act and deed in said capacity.

Before me,

Notary Public / Attorney at Law

Print Name:

Mail this certification to the Town's Enforcement Authority at the following address:

Town of Cape Elizabeth

320 Ocean House Road

P.O. Box 6260

Cape Elizabeth, Maine 04107